## Slide 1
ECE 1710: Power Distribution Systems Engineering and Smart Grids
Lecture 4
Dr. Robert Kerestes
University of Pittsburgh
Swanson School of Engineering
Department of Electrical and Computer Engineering
Notes: Instructions for editing school and department titles:
Select from menu: View > Master > Slide Master
Click on each text area you wish to edit. Text will become editable.

## Slide 2: Outline
Module #1: Voltage drop
Module #2: Line impedance
Module #3: Three-Phase Circuit Caluculations
Module #4: Linear Ladder Network
Module #5: Ladder Iterative Power Flow

## Slide 3
Learning Objectives:
  Use phasor diagrams to visually describe voltage drops in electric power systems.
  Carry out impedance calculations for transposed overhead transmission lines.
  Calculate single-phase ratings based off of three-phase ratings
  Calculate the voltages of a linear ladder network
  Perform a power flow for a nonlinear ladder network
Learning Objectives

## Slide 4: Voltage drop

## Slide 5: Voltage Drop
In distribution systems, a feeder provides service to unbalanced three-phase, two-phase, and single-phase loads over untransposed three-phase, two-phase, and single-phase line segments.
Leads to unbalanced three-phase voltages and currents.
Requires accurate modeling, for highest fidelity models symmetrical components will not work
Often an approximate model will suffice. These models assume:
  Balanced loads
  Perfectly transposed line segments.

## Slide 6: Voltage Drop
A line-to-neutral equivalent circuit of a three-phase line segment serving a balanced three-phase load is shown below:
Voltage drop is defined as:

## Slide 7: Voltage Drop
Using KVL we have

## Slide 8: Voltage Drop
Using phasors we can approximate voltage drop:
Note: Most power systems loads are lagging, so the current lags the voltage at the load.

## Slide 9: Voltage Drop
As long as is small, as is the case with most distribution circuits, we can say that

## Slide 10
Example: For the system shown below, assume the voltage at N1 is 2400 V, the line impedance of the 1st line segment is Z12 = 0.2841 + j0.5682 Ω, and the current flowing through the segment is I12 = 43.0093∠-25.8419 A.
a.) Using the voltage calculated in the last lecture for V2 ( =V) compute the exact Vdrop across N1-N2
b.) Compute the approximate Vdrop using Re{ZI} .
c.) Calculate the percent error between the two.

## Slide 11
Solution: (a) Using the formula , we have
(b) Recall the impedance of the line for the first segment is . Using the formula , we have

## Slide 12
(c) The percent error between the two methods is

## Slide 13: Line impedance

## Slide 14: Line impedance
Types of Power Lines
Transmission Level [1]
Distribution Level [2]

## Slide 15: Line impedance
For the approximate modeling of a line segment, it will be assumed that the line segment is transposed. This means that the line is balanced (meaning the impedance in each phase is equal.
a
a
a
b
b
b
c
c
c
Line Transposition

## Slide 16
A typical three-phase line configuration

## Slide 17: Line impedance
The equation for the positive sequence impedance is given by
where

## Slide 19: Line impedance

## Slide 20: Line impedance

## Slide 21: Line impedance
Conductor type
GMR
Resistance

## Slide 22: Line impedance
Solution:

## Slide 23: Line impedance
For the pole shown, the conductors are 250,000 cm, CON Lay, and AA. The nominal line-to-line voltage of the feeder is 14.4 kV.
Question: What is the resistance per mile?

## Slide 24: Line impedance
For the pole shown, the conductors are 250,000 cm, CON Lay, and AA. The nominal line-to-line voltage of the feeder is 14.4 kV.
Question: What is GMR?

## Slide 25: Line impedance
For the pole shown, the conductors are 250,000 cm, CON Lay, and AA. The nominal line-to-line voltage of the feeder is 14.4 kV.
Question: Calculate and round to two decimal places

## Slide 26: Line impedance
Question: Calculate and round to two decimal places

## Slide 27: Three-Phase Circuit Calculations

## Slide 28: Three-Phase Circuit Calculations
As we’ve seen earlier in this lecture, some parts of power systems circuits have three-phases
Module #5
Relationship between line-to-line and line-to-ground voltages
Line-to-ground voltage
Line-to-line voltage

## Slide 29: Three-Phase Circuit Calculations
The currents in each of the lines are denoted by . Since the circuit is balanced, each of the voltages and currents are equal for each phase. We can then calculate real power using
Module #5

## Slide 30: Three-Phase Circuit Calculations
However, if we want to use rms line-to-line voltages instead we can replace the rms line-to-ground voltages with
Module #5
substituting

## Slide 31: Three-Phase Circuit Calculations
We can do the same thing with reactive and apparent power giving us
Module #5
or
or
or

## Slide 32: Three-Phase Circuit Calculations
Note ratings of equipment and in power systems is almost always given in terms of line-to-line voltages!!
However, you should be familiar with both line-to-line and line-to-ground voltage levels.
Module #5

## Slide 33: Linear Ladder Network

## Slide 34: Distribution System Power Flow
A distribution feeder is non-linear because most loads are assumed to be constant kW and kvar. However, the approach taken for a linear system can be modified to account for the non-linear characteristics of the distribution feeder.
Linear Ladder Network

## Slide 35: Linear Ladder Network
First let’s look at a linear network to compare. The loads here are defined as constant impedance loads.
Linear Ladder Network

## Slide 36: Linear Ladder Network
Linear Ladder Network
This systems has line impedances of:
This system has load impedances of:

## Slide 37: Linear Ladder Network
Linear Ladder Network
Initially start with all currents equal to zero:
This means all voltages are the same

## Slide 38: Linear Ladder Network
Linear Ladder Network
We can then ”update” the voltages and currents using ohm’s law and KVL. For example

## Slide 39: Linear Ladder Network
Linear Ladder Network
We can then ”update” the voltages and currents using ohm’s law and KVL. For example

## Slide 40: Linear Ladder Network
Linear Ladder Network
We then continue the process back to the source voltage computing

## Slide 41: Linear Ladder Network
This algorithm is shown in the following Mathcad routine
However, we know the source voltage is 7200 volts rather than the load, therefore we need to correct this

## Slide 42: Linear Ladder Network
The ratio of source to load is
We can use the to correct for a source voltage of 7200 V:

## Slide 43: Linear Ladder Network
The ratio of source to load is

## Slide 44: Linear Ladder Network
Running the algorithm again with the new start values produces

## Slide 45: Linear Ladder Network
And a voltage drop% of

## Slide 46: Ladder Iterative Power Flow

## Slide 47: Ladder Iterative Power Flow
The power flow problem is a nonlinear circuit analysis problem as opposed to a linear circuit analysis problem that a student may be familiar with from a circuits class.
Power Flow Program
Inputs:
        Load power (kW & kvar, kW & pf, or kVA & pf)
        Equipment impedances and connections
        Source voltage levels
    Outputs (calculates):
        System voltages
        System currents
        System power flows and losses

## Slide 48: Ladder Iterative Power Flow
The following shows a nonlinear network. This is similar to the linear network covered in the previous module, however, the loads are now constant power loads rather than constant impedance.
Nonlinear Ladder Network

## Slide 49: Ladder Iterative Power Flow
Due to the nonlinear nature of the network, we will now have to iterative towards a solution.
This iterative process is called the forward sweep-backward sweep.
Nonlinear Ladder Network

## Slide 50: Ladder Iterative Power Flow
For the forward sweep, we will start by assuming all currents are zero and compute the voltage at all of the nodes
Nonlinear Ladder Network
Forward Sweep

## Slide 51: Ladder Iterative Power Flow
After the forward sweep, we will then compute all load currents using the following equation
Nonlinear Ladder Network

## Slide 52: Ladder Iterative Power Flow
The backward sweep will then compute all currents all the way back to the source current
Nonlinear Ladder Network
Backward Sweep

## Slide 53: Ladder Iterative Power Flow
These currents can be calculated starting at the last node working backwards, using the equation
Nonlinear Ladder Network

## Slide 54: Ladder Iterative Power Flow
We then perform the forward sweep again, except this time the currents are nonzero so we will use KVL to calculate each voltage using
Nonlinear Ladder Network
Forward Sweep

## Slide 55: Ladder Iterative Power Flow
We then continue to iterate through the forward sweep-backward sweep until our solution has converged. That is
where

## Slide 56: Ladder Iterative Power Flow
For an example, we will use the same system as in the linear network example, but will change the loads to be constant power.
Our convergence tolerance will be

## Slide 57: Ladder Iterative Power Flow
Starting with a voltages and currents equal to zero for the zeroth iteration i.e.
and

## Slide 58: Ladder Iterative Power Flow
For the first forward sweep, since all currents are zero we get
Before calculating our currents we need to check our error

## Slide 59: Ladder Iterative Power Flow
Then calculating the load currents with
we get

## Slide 60: Ladder Iterative Power Flow
We then perform the backward sweep using
we get

## Slide 61: Ladder Iterative Power Flow
We then increment the iteration n and run through he sweep again, i.e.
Forward Sweep
Check convergence criteria
If no, update ”old” voltages

## Slide 62: Ladder Iterative Power Flow
We then increment the iteration n and run through he sweep again, i.e.
Then calculate load currents
Backward sweep
Increment iteration n and repeat

## Slide 63: Ladder Iterative Power Flow
After four iterations our solution converges with

## Slide 64: Ladder Iterative Power Flow

## Slide 65: Reference Materials
[1] "Power transmission lines" by Oran Viriyincy is licensed under CC BY-SA 2.0.
[2] "Telephone-Pole-and-Electric-Powerlines-with-Cloudy-Storm-Sky" by Captain Kimo is licensed under CC BY-NC-ND 2.0.